## Slide 1: Accelerating Homomorphic Evaluation on Reconfigurable Hardware
Thomas Pöppelmann, Michael Naehrig, Andrew Putnam, Adrian Macias

## Slide 2: Outline
Motivation
Somewhat Homomorphic Encryption
Implementation
Results
Conclusion
1
2
3
4
5

## Slide 3: Outline
Motivation
Somewhat Homomorphic Encryption
Implementation
Results
Conclusion
1
2
3
4
5

## Slide 4: Motivation: Secure Computation
Homomorphic encryption allows computation on data without revealing the data itself to the entity performing the computation
Premium example: cloud computing
  Clients encrypt data and store encrypted data in the cloud
  The cloud server performs computation but an attacker (malicious admin, hacker, intelligence agency) cannot see the actual data
  The client just gets the result
Practical usable for specialized, high risk, or privacy sensitive applications
    Genomic data processing
    Medical data processing
    Machine learning

## Slide 5: Motivation: Homomorphic evaluation
5
10
20
Encrypt
Encrypt
Encrypt
?
?
?
ADD
MUL
MUL
?
Decrypt
1500
ADD
?
Decrypt
80
Untrusted environment, e.g., the cloud
SW
SW
Evaluation
This work: How can we use FPGAs to accelerate
homomorphic evaluation?

## Slide 6: Outline
Motivation
Somewhat Homomorphic Encryption
Implementation
Results
Conclusion
1
2
3
4
5

## Slide 7: YASHE
YASHE [BLLN’13]: Yet Another Somewhat Homomorphic Encryption scheme
For each evaluation operation (addition/multiplication) noise in cipher text grows
  At some point the noise gets too large and original message cannot be recovered anymore => manage noise growth
  Somewhat homomorphic scheme (SHE) => amount of computations is limited by choice of parameters
Security based on decisional small polynomial ratio (DSPR) and ring learning with errors assumption (RLWE)
Operations on (large) polynomials
[BLLN’13] ]Joppe W. Bos, Kristin Lauter, Jake Loftus, Michael Naehrig: Improved Security for a Ring-Based Fully Homomorphic Encryption Scheme. IMACC 2013,

## Slide 8: YASHE’ Algorithms
Setup and encryption/decryption:
ParamsGen(): Generate parameters based on a security parameter
KeyGen(params): Generate a public key a private key , and evaluation key
Encrypt(): The message space is for a small . Sample noise vectors . Return
Decrypt(): Return ] mod t.
Ciphertext evaluation:
Add( Return
Mult( Compute RMult() and return KeySwitch(, )
  RMult(): return
  KeySwitch(, ) : Return

## Slide 9: YASHE RMult
Ciphertext evaluation:
c’
polynomial
multiplication
Multiplication by scalar and rounding
n
log(q)
  Reduction modulo but no mod q

## Slide 10: YASHE KeySwitch
Ciphertext evaluation:
Several polynomial multiplications by constant evaluation key
is split into several polynomials
Size determined by parameter window parameter

## Slide 11: YASHE (Selected) Parameters
Description | Parameter | Set-I | Set-II
Polynomial coefficients | n | 4096 | 16384
Modulus | q |  | 
Plaintext space | t | 1024 | 1024
Windows size | w |  | 
Evaluation keys | q/w | 1 | 8
Supported multiplications (levels) | L | 1 | 9
Size of one polynomial | - | 62 KB | 1 MB
Size of evaluation key | - | 124 KB | 8 MB
Description | Parameter | Set-I | Set-II
Polynomial coefficients | n | 4096 | 16384
Modulus | q |  | 
Plaintext space | t | 1024 | 1024
Windows size | w |  | 
Evaluation keys | q/w | 1 | 8
Supported multiplications (levels) | L | 1 | 9
Size of one polynomial | - | 62 KB | 1 MB
Size of evaluation key | - | 124 KB | 8 MB
Parameters are supposed to provide at least 80 bits of security

## Slide 12: Outline
Motivation
Somewhat Homomorphic Encryption
Implementation
Results
Conclusion
1
2
3
4
5

## Slide 13: Target Platform: Catapult
Microsoft project [PCC+14] to accelerate cloud services using Altera Stratix V FPGAs
  Each server contains an FPGA
  FPGAs are connected by complex dedicated communication network
2x throughput over software-only Bing ranking in 1632 server/FPGA prototype
Of independent interest to CHES community
[PCC+14] Andrew Putnam et al, A Reconfigurable Fabric for Accelerating Large-Scale Datacenter Services. ISCA 2014

## Slide 14: Implementation Challenges on FPGAs
Target device: Stratix V
  172,600 ALMs (logic blocks)
  4.9 MB internal memory
  1590 embedded multipliers
Implementation Challenge
  Usage of external memory
  Large multipliers required (e.g., 512x512-bits)
  Development more complex
FPGA
(4 MB)
DRAM0
(4 GB)
DDR
PC
PCIe
DRAM1
(4 GB)
DDR
Evaluation operations

## Slide 15: Number Theoretic Transform
Polynomial multiplication using the number theoretic transform (NTT)
  NTT is a fast Fourier transformation (FFT) in (no complex or floating point numbers)
  with
  Using a certain scaling we do not need zero padding (we can multiply coefficient polynomials using n-point NTT)

## Slide 16: Cached-NTT
Cached-NTT
  Splits computation of NTT into two epochs
  Performs computation locally on groups
  After all groups of one epoch are computed a reordering step is necessary
multiplications by constants (twiddle factors)
additions/subtractions

## Slide 17: Architecture
NttCore computes one or several groups of NTT in parallel
NTTButterfly implements pipelined 512x512-bit multiplier (supports also 1040x1040-bit in 4 cycles)
Dual buffering of data set in FPGA to support computation and memory access in parallel
Microcode engine wit approx. 15 instructions

## Slide 18: Outline
Motivation
Somewhat Homomorphic Encryption
Implementation
Results
Conclusion
1
2
3
4
5

## Slide 19: Results
SET II implementation requires 141,090 (82%) ALMs, 577 (36%) DSPs and 17,626,400 (43%) BRAM bits on Altera Stratix V
Congested design and constraints of DRAM and PCIe controller result in relatively low clock frequency
Cycle counts measured online to account for DRAM latency
Implementation | Mult | Add
Set I (n=4096) @100 MHz | 675,326 cycles | 19,057 cycles
 | 6.75 ms | 0.19 ms
Set II (n=16384) @66 MHz | 3,212,506 cycles | 61,775 cycles
 | 48.67 ms | 0.94 ms

## Slide 20: Comparison
[LN14] Tancrède Lepoint, Michael Naehrig: A Comparison of the Homomorphic Encryption Schemes FV and YASHE. AFRICACRYPT 2014
[RJVDV’15] Roy et al. Modular Hardware Architecture for Somewhat Homomorphic Function Evaluation. CHES 2015
Author | Parameter | Architecture | Mult | Add
Our work | YASHE, n=16384 | FPGA (Stratix 5) | 49 ms | 1 ms
[LN’14] | YASHE, n=4096 | 3.5 GHz Intel i7 | 49 ms | 0.7 ms
[RJVDV’15] | YASHE, n=32768 | FPGA (Virtex-7) | 112 ms | 0.17 ms
Schemes and parameters differ widely
Costs of FPGAs are hard to compare (FPGA+I/O+board)
Numerous ASIC, GPU implementations published while schemes got better and better

## Slide 21: Outline
Motivation
Somewhat Homomorphic Encryption
Implementation
Results
Conclusion
1
2
3
4
5

## Slide 22: Conclusion
Cached-FFT/NTT solves problem of limited on-chip memory
Large multiplier (1040x1040) is a bottleneck => Chinese remainder theorem (see next talk)
Biggest effort/time was spend on external memory interface
  Has to be taken into account for evaluation of costs and performance
  Simulation and debugging more complex

## Slide 23: Future Work
Further evaluation of different implementation techniques (maybe CRT+cached-NTT)
Exploration of different and larger parameter sets
Can evaluation operations (MUL/ADD) be performed directly in frequency (NTT/FFT) domain
Multi-FPGA design or specialized board
FPGA
FPGA
FPGA
RAM
RAM
RAM
RAM

## Slide 24: Thank You
Thank you for your attention!
Any Questions?
Contact:
thomas.poeppelmann@Infineon.com
Full paper:
https://eprint.iacr.org/2015/631