## Slide 1: Stealing Keys from PCs using a Radio: Cheap Electromagnetic Attacks on Windowed Exponentiation
Daniel Genkin
Technion and Tel Aviv University
Eran Tromer
Tel Aviv University
Itamar Pipman
Tel Aviv University
joint work with
Lev Pachmanov
Tel Aviv University

## Slide 2: Side channel attacks
electromagnetic
probing
optical
power
CPU architecture
Notes: Fix power analysis fluke

## Slide 3: Problems with Attacking PCs
Different scenario
  Not handed out to the adversary
  Attacker needs to be swift and inconspicuous
Speed
  2GHz CPU
  Clock-rate attacks requires expansive and bulky equipment (compared to a 100 MHz smart card)
Complexity & Noise
  Complex electronics running complicated software (in parallel)
vs.
$100,000
$1,000
vs.
vs.

## Slide 4: Physical side-channel attacks on PCs
Non-cryptographic: [Oren Shamir 06], [Clark Mustafa Randford Sorber Fu Xu 13], [Zajic Prvulovic 14], [Guri Kachlon Hasson Kedma Mirsky Elovici 15] [Guri Monitz Mirski Elovici 15], [Masti Rai Ranganathan Muller Thiele Capkun 15]
Cryptographic:
Algorithm | Attack type | #ciphertexts | Time | BW | Cipher | Ref
SQR-and- always-MUL | Adaptive chosen ciphertext |  | 1 hour | 50 kHz | RSA | [Genkin Shamir Tromer’14]
Algorithm | Attack type | #ciphertexts | Time | BW | Cipher | Ref
SQR-and- always-MUL | Adaptive chosen ciphertext |  | 1 hour | 50 kHz | RSA | [Genkin Shamir Tromer’14]

## Slide 5: Physical side-channel attacks on PCs
Non-cryptographic: [Oren Shamir 06], [Clark Mustafa Randford Sorber Fu Xu 13], [Zajic Prvulovic 14], [Guri Kachlon Hasson Kedma Mirsky Elovici 15] [Guri Monitz Mirski Elovici 15], [Masti Rai Ranganathan Muller Thiele Capkun 15]
Cryptographic:
Modern implementations use windowed exponentiation (fixed or sliding window)
Attacks require either:
  simple equipment , slow
  lots of expensive equipment, fast
Algorithm | Attack type | #ciphertexts | Time | BW | Cipher | Ref
SQR-and- always-MUL | Adaptive chosen ciphertext |  | 1 hour | 50 kHz | RSA | [Genkin Shamir Tromer’14]
SQR-and- always-MUL | Non-adaptive chosen ciphertext |  | 3 sec | 2 MHz | ElGamal, RSA | [Genkin Pipman Tromer’14]
Algorithm | Attack type | #ciphertexts | Time | BW | Cipher | Ref
SQR-and- always-MUL | Adaptive chosen ciphertext |  | 1 hour | 50 kHz | RSA | [Genkin Shamir Tromer’14]
SQR-and- always-MUL | Non-adaptive chosen ciphertext |  | 3 sec | 2 MHz | ElGamal, RSA | [Genkin Pipman Tromer’14]

## Slide 6: Physical side-channel attacks on PCs
Non-cryptographic: [Oren Shamir 06], [Clark Mustafa Randford Sorber Fu Xu 13], [Zajic Prvulovic 14], [Guri Kachlon Hasson Kedma Mirsky Elovici 15] [Guri Monitz Mirski Elovici 15], [Masti Rai Ranganathan Muller Thiele Capkun 15]
Modern implementations use windowed exponentiation (fixed or sliding window)
Attacks require either:
  simple equipment , slow
  lots of expensive equipment, fast
Algorithm | Attack type | #ciphertexts | Time | BW | Cipher | Ref
SQR-and- always-MUL | Adaptive chosen ciphertext |  | 1 hour | 50 kHz | RSA | [Genkin Shamir Tromer’14]
SQR-and- always-MUL | Non-adaptive chosen ciphertext |  | 3 sec | 2 MHz | ElGamal, RSA | [Genkin Pipman Tromer’14]
Algorithm | Attack type | #ciphertexts | Time | BW | Cipher | Ref
SQR-and- always-MUL | Adaptive chosen ciphertext |  | 1 hour | 50 kHz | RSA | [Genkin Shamir Tromer’14]
SQR-and- always-MUL | Non-adaptive chosen ciphertext |  | 3 sec | 2 MHz | ElGamal, RSA | [Genkin Pipman Tromer’14]
Cryptographic:

## Slide 7: Physical side-channel attacks on PCs
Cryptographic:
This work:
Equipment cost: <$300
  can be done with a simple radio
Effective on common cryptographic software
  GnuPG 1.4.18, CVE 2014-3591
Algorithm | Attack type | #ciphertexts | Time | BW | Cipher | Ref
SQR-and- always-MUL | Adaptive chosen ciphertext |  | 1 hour | 50 kHz | RSA | [Genkin Shamir Tromer’14]
SQR-and- always-MUL | Non-adaptive chosen ciphertext |  | 3 sec | 2 MHz | ElGamal, RSA | [Genkin Pipman Tromer’14]
Algorithm | Attack type | #ciphertexts | Time | BW | Cipher | Ref
SQR-and- always-MUL | Adaptive chosen ciphertext |  | 1 hour | 50 kHz | RSA | [Genkin Shamir Tromer’14]
SQR-and- always-MUL | Non-adaptive chosen ciphertext |  | 3 sec | 2 MHz | ElGamal, RSA | [Genkin Pipman Tromer’14]
Sliding window | Non-adaptive chosen ciphertext | 8 or 16 ( for -bit window) | 30 sec | 100 kHZ | ElGamal, RSA | This paper
Fixed window |  |  |  |  |  | 
Sliding window | Non-adaptive chosen ciphertext |  | 30 sec | 100 kHZ | ElGamal, RSA | This paper
Fixed window |  |  |  |  |  | 

## Slide 8: Attacking ElGamal

## Slide 9: ElGamal encryption
Key setup
pk: prime , generator for , for a random .
sk:
Encryption
Decryption

## Slide 10: Fixed-window modular exponentiation
modular_exponentiation(c,x,p){
// Compute lookup table: a[0] = 1
a[1] = c mod p
a[2] = c2 mod p
…
a[i] = ci mod p
…
a[2w] = c mod p
// Process x in blocks:
m=1, j=1
while (j n) do
for k=1 to w do
m = m2 mod p
m = m*a[xj…xj+w] mod p
j=j+w+1
return m
}
2w
depends on both xj…xj+w and and is used for mult
craft to affect the mult, based on xj…xj+w
measure changes inside mult operation and obtain xj…xj+w
  2GHz CPU speed vs. 100kHz measurements
can only see drastic changes inside mult operation
  Idea: leakage self-amplification
  abuse algorithm’s own code to amplify its own leakage!
  Craft suitable cipher-text to affect the inner-most loop
  Small differences in repeated inner-most loops cause a big overall difference in code behavior

## Slide 11: Fixed-window modular exponentiation
modular_exponentiation(c,x,p){
// Compute lookup table: a[0] = 1
a[1] = c mod p
a[2] = c2 mod p
…
a[i] = ci mod p
…
a[2w] = c mod p
// Process x in blocks:
m=1, j=1
while (j n) do
for k=1 to w do
m = m2 mod p
m = m*a[xj…xj+w] mod p
j=j+w+1
return m
}
2w
karatsuba_mult(a,b){
…
basic_mult(a,b)
…
}
basic_mult(a,b){
…
}
if (b[j]==0)
continue else return b[j]*a
~x7
~x9
repeated ~200 times per mult
~0.2ms of measurements per mult
Recover the key by poisoning each table index, one at a time
For each :
Choose s.t: has many zero limbs
Every time that xj…xj+w = the second operand has many zero limbs
Measure and deduce occurrences of in secret key

## Slide 12: Demo: ElGamal key extraction

## Slide 13: Portable Instrument for Trace Acquisition (PITA)
Cost: $300

## Slide 14: Electromagnetic attacks

## Slide 15: Leaking the secret key
carrier
FM-modulated key
due to multiplications of a random-looking /
mostly zero limb value of

## Slide 16: ElGamal Key Extraction
After frequency demodulation
  Corruptions every ~15ms (corresponding to the time interrupt)
  Gradual drifts

## Slide 17: ElGamal Key Extraction
After frequency demodulation
  Corruptions every ~15ms (corresponding to the time interrupt)
  Gradual drifts
After averaging (ignoring corruptions and correcting drifts)
After equalization

## Slide 18: ElGamal Key Extraction
0x1
0x3
0x5
x=???????5??3?3?1?????????5????5??????5????3??????5???5???????
Window value

## Slide 19: Key extraction via commodity radio receiver

## Slide 20: Key extraction from 50cm away

## Slide 21: Thanks!
tau.ac.il/~tromer/radioexp

## Slide 22: Thanks!
tau.ac.il/~tromer/radioexp

## Slide 23: Thanks!
tau.ac.il/~tromer/radioexp

## Slide 24: Thanks!
tau.ac.il/~tromer/radioexp

## Slide 25: Thanks!
tau.ac.il/~tromer/radioexp