## Slide 1
16.09.2015
CHES 2015
Finding the AES Bits in the Haystack:
Reverse Engineering and SCA Using Voltage Contrast
Christian Kison, Jürgen Frinken and Christof Paar

## Slide 2: Voltage Contrast SCA Outline
Motivation
Voltage Contrast
  Passive/Active Voltage Contrast (VC)
  Capacitive Coupled Voltage Contrast (CCVC)
Voltage Contrast Side Channel Analysis (VCSCA)
  Hardware Reverse Engineering
  Correlation Attack
Conclusion and Future Work

## Slide 3: Voltage Contrast SCA Motivation – The Haystack
Goal: Hardware Reverse Engineering
Straightforward Approach
  Sand-and-scan
  Netlist extraction
  Search Region-of-Interest (ROI)
Todays IC chips
  Millions of Gates
  ROI Location: Needle in the haystack
  Infeasible manual work
  http://edocumentsciences.com/wp-content/uploads/2011/10/Finding-A-Password-In-A-Haystack.jpg

## Slide 4: Voltage Contrast SCA Region of Interest – The Needle
Finding the ROI (Region of Interest) :
  Mandatory for Hardware Reverse Engineering
  Precise Fault Attacks
    Laser, UV light, EM induction, Probing, …
  Improves EM SCA
Multiple approaches suggested:
  EM cartography
  Photon Emission Images
  Surface Liquid Crystal
  Fault Attacks
  Voltage Contrast / E-Beam
FLASH
RAM
ANALOG IO
AES??

## Slide 5: Voltage Contrast SCA Voltage Contrast - Introduction
Voltage Contrast used for Failure Analysis
  Locate badly connected wires
  High resistance
  …
Negative charge of electrons in beams
  Commercial E-Beam Prober
    Very fast
    Expensive
    Non-contact voltmeter
  Scanning Electron Microscope (SEM)
    Slow
    Mid-cost
    Academically well distributed
http://www.nationalparts.com/pes/images/failure_analysis.jpg

## Slide 6: Voltage Contrast SCA Voltage Contrast - ROI
Target: Atmel XMega
  AES Co-Processor
  Proof of Concept
Decap package
  Top layer visible
XMega in SEM vacuum chamber
Power-up device
Trigger AES
http://jeffreyhill.typepad.com/.a/6a00d8341d417153ef016768405219970b-800wi
http://www.muanalysis.com/_documents/300%20series%20images/304.jpg

## Slide 7: Voltage Contrast SCA Passive/Active Voltage Contrast
-
-
-
-
-
primary beam
-
-
-
-
-
primary beam
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
+
+
+
Structure
Grounded structure
SEM
SEM
-
-
-
-
-
-
-
secondary electrons
imaging
detector
imaging
detector
secondary electrons
-
-
-

## Slide 8: Voltage Contrast SCA VCA in a SEM
Neutral (not connected)
Working (cycle x)
Working (cycle x+1)
Slow SEM
  Some kHz
  External clock control!
Notes: Suche nach einem Grashalm auf einem Fußballfeld
The effect of setting the lock bits by UV-light is used to find it’s location.
If the lock bit is set it is not under the mask. Otherwise it is in the covered area.
Using the effect of setting the lock bits by UV-light it is possible to find the location of interest.
Therefore we cover the half of the interesting area with an UV-absorbing mask, irradiate with UV-light for some minutes and read the lock bit.
If the lock bit is set we know that it is not under the mask. Otherwise it is in the covered area.
repeat this until the handling of the mask is to difficult.

## Slide 9: Voltage Contrast SCA Setup – Low Cost SEM Control
SEM (2)
primary beam
DUT
(1)
Controller
(3)
generated clock
SEM Control PC
(2)
Keyboard
emulation
PC
(4)
setup
USART
Notes: Suche nach einem Grashalm auf einem Fußballfeld
The effect of setting the lock bits by UV-light is used to find it’s location.
If the lock bit is set it is not under the mask. Otherwise it is in the covered area.
Using the effect of setting the lock bits by UV-light it is possible to find the location of interest.
Therefore we cover the half of the interesting area with an UV-absorbing mask, irradiate with UV-light for some minutes and read the lock bit.
If the lock bit is set we know that it is not under the mask. Otherwise it is in the covered area.
repeat this until the handling of the mask is to difficult.

## Slide 10: Voltage Contrast SCA Capacitive Coupled Voltage Contrast
Capacitive Coupled Voltage Contrast
  With passivation
  2 phases separated by a cycle
    Charge
    (Clock cycle)
    Evaluate
External clock control!
dielectric
SiO2
Wire
Wire
Wire
Top metal layer
2nd metal layer
Schematic
Notes: Suche nach einem Grashalm auf einem Fußballfeld
The effect of setting the lock bits by UV-light is used to find it’s location.
If the lock bit is set it is not under the mask. Otherwise it is in the covered area.
Using the effect of setting the lock bits by UV-light it is possible to find the location of interest.
Therefore we cover the half of the interesting area with an UV-absorbing mask, irradiate with UV-light for some minutes and read the lock bit.
If the lock bit is set we know that it is not under the mask. Otherwise it is in the covered area.
repeat this until the handling of the mask is to difficult.

## Slide 11: Voltage Contrast SCA Capacitive Coupled VC – Phase 1
Top metal layer
dielectric
SiO2
+3 V
GND
+3 V
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
accumulated charge
-
-
-
-
+
+
+
+
+
+
+
+
-
+
+
Secondmetal
layer
SEM
-
-
-
-
-
primary beam
-
-
Schematic
Notes: Suche nach einem Grashalm auf einem Fußballfeld
The effect of setting the lock bits by UV-light is used to find it’s location.
If the lock bit is set it is not under the mask. Otherwise it is in the covered area.
Using the effect of setting the lock bits by UV-light it is possible to find the location of interest.
Therefore we cover the half of the interesting area with an UV-absorbing mask, irradiate with UV-light for some minutes and read the lock bit.
If the lock bit is set we know that it is not under the mask. Otherwise it is in the covered area.
repeat this until the handling of the mask is to difficult.

## Slide 12: Voltage Contrast SCA Capacitive Coupled VC – Phase 2
Top metal layer
dielectric
SiO2
GND
+3V
GND
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
-
+
Secondmetal
layer
Note: Clock cycle takes place
SEM
-
-
-
-
-
-
primary beam
(accumulated)
secondary electrons
-
-
-
Schematic
Notes: Suche nach einem Grashalm auf einem Fußballfeld
The effect of setting the lock bits by UV-light is used to find it’s location.
If the lock bit is set it is not under the mask. Otherwise it is in the covered area.
Using the effect of setting the lock bits by UV-light it is possible to find the location of interest.
Therefore we cover the half of the interesting area with an UV-absorbing mask, irradiate with UV-light for some minutes and read the lock bit.
If the lock bit is set we know that it is not under the mask. Otherwise it is in the covered area.
repeat this until the handling of the mask is to difficult.

## Slide 13: Voltage Contrast SCA A Single Tracevideo – 5 Frames / 1 Clock cycle
Notes: Suche nach einem Grashalm auf einem Fußballfeld
The effect of setting the lock bits by UV-light is used to find it’s location.
If the lock bit is set it is not under the mask. Otherwise it is in the covered area.
Using the effect of setting the lock bits by UV-light it is possible to find the location of interest.
Therefore we cover the half of the interesting area with an UV-absorbing mask, irradiate with UV-light for some minutes and read the lock bit.
If the lock bit is set we know that it is not under the mask. Otherwise it is in the covered area.
repeat this until the handling of the mask is to difficult.

## Slide 14: Voltage Contrast SCA Proof-of-Concept
We know:
  Key
  Plaintext/Ciphertext
Traces:
  Tracevideo frames
Pearson correlation
  Hamming Weight model
    Intermediate AES bits and raw VCSCA videoframe
    2-bit logic functions of intermediate bits ( SCA Reverse Engineering)
    Simple Side Channel Analysis (single trace, nor plain/key known)
Trace Acquisition
  300 Traces
  ~3 Hz external clock
T1
T2
T300
Tracevideos
Frames
F1
F2
F…
Fn
Correlate
Intermediate AES bits
Located correlation frame
T…

## Slide 15: Voltage Contrast SCA Results – Locate Bit 1 of Subbytes Byte 1
Frame 48
  Subbytes
  Byte 1
  Bit 1
Frame 48
  Subbytes
  Byte X
  Bit 1
Sequentially byte-wise pipelined
Common Load/Store Unit

## Slide 16: Voltage Contrast SCA Results - Hardware Reverse Engineering
SEM pictures
  1st and 2nd layer
  Overlayed with 50% transparent result (dark cloud)
Align and Trace down
  DFFs
  …
Mark in extracted netlist

## Slide 17: Voltage Contrast SCA Results – Correlation Attack
New Assumption:
  Key unknown
  Known plaintext
Aquire 100 Traces
Key Hypothesis
  Set to 1
  Correlation close to -1 or +1
Full AES-128 key recovered

## Slide 18: Voltage Contrast SCA Conclusion
Voltage Contrast is mid-cost
  Scanning Electronic Microscope
    Widely available in academia
    Second hand for < €10k
  Low cost adjustment
Hardware Reverse Engineering tool
  Pinpoint ROI within minutes
  Front side
    Might be shielded
Powerful Side Channel (VCSCA)

## Slide 19: Voltage Contrast SCA Future Work
Hardware Reverse Engineering Tool
  Optimize the setup
    Faster
    Less noisy
  Verify netlist assumptions
Hardware Debugging tool?
Research shows feasibility of backside CCVC[1]
[1] Schlangen et.al, Backside e-beam probing on nano scale devices, Journal of Materials Science: Materials in Electronics

## Slide 20: Thank You! Questions?