## Slide 1
Fault Analysis of Cryptosystems:
Attacks, Countermeasures, and Metrics
Debdeep Mukhopadhyay
Sikhar Patranabis
Department of Computer Science and Engineering
IIT Kharagpur
debdeep@cse.iitkgp.ernet.in
sikhar.patranabis@cse.iitkgp.ernet.in
http://cse.iitkgp.ac.in/resgrp/seal/

## Slide 3
Fault Tolerance : Context in Cryptography
High-throughput requirements of various information disciplines.
Cryptographic accelerators are needed
  Hardware Designs implemented as ASICs and FPGAs.
  Raises concerns regarding their reliability.
Faults are catastrophic in context to security algorithms.
  AES can be broken with a single well-formed fault!

## Slide 4: Types of Fault Attacks
Differential Fault Analysis (DFA)
  Induce a fault
  Observe the Difference of the correct and faulty pairs
  Derive equations to obtain the key
Differential Fault Intensity Attack (DFIA)
  Obtain non-uniform faults (biased faults) through non-expensive techniques
  Perform Side Channel Analysis like power analysis to exploit the bias

## Slide 5: Fault Tolerant Architecture
Countermeasures to DFA
Detection Based Countermeasures
Based on application of Classical fault tolerant techniques to cryptography
Uses Various Forms of Redundancy
Infection Based Countermeasures
Tries to disturb the information of a fault by infection
No explicit detection step

## Slide 6: Outline
Part 1: Brief History of Fault Attacks, Fault Models
Part 2: Differential Fault Analysis of Block Ciphers
Part 3: Countermeasures versus Biased Faults – Pushing the Limits
Part 4 : Fault Tolerance at a Granular Level : Idempotent Instruction Sequences
Part 5: Metrics for Fault Analysis

## Slide 7: Brief History of Fault Attacks, Fault Models
PART 1

## Slide 8: Techniques: Cryptographic Algorithms
ATTACKER
Key
(e)
encrypt
plaintext message
retreat at dawn
Key
(d)
decrypt
ciphertext
plaintext message
retreat at dawn
SENDER
ciphertext
sb%6x*cmf
RECEIVER

## Slide 9: Fault Attacks : A Brief Overview
Introduction of faults in the normal execution of cryptographic algorithms and analysis of faulty output to obtain the key
First conceived in 1996 by Boneh, Demillo and Lipton
E. Biham developed Differential Fault Analysis (DFA) of DES
Today there are numerous examples of fault analysis of block ciphers such as AES under a variety of fault models and fault injection techniques
Popular Fault Injection Techniques – Clock Glitches, Voltage Glitches, EM and Optical Injection Techniques

## Slide 10: Fault Attacks on RSA (Boneh et al. 1996)
Only decryption is subject to attacks
Assume:
  1. Attacker can flip a single bit in key d 2. S and corresponding message M known to attacker
  Decryption device generates satisfying
  If then
  If then
Source : Koren and Krishna, Morgan-Kaufman 2007

## Slide 11: Fault Attacks on RSA (contd.)
  Assume that the attacker flips randomly a bit in d.
Example: (e,N)=(7,77), d=43
  Ciphertext=37 producing M=9 if no fault is injected and if a fault is injected
  Search for i such that i=3 since
Source : Koren and Krishna, Morgan-Kaufman 2007

## Slide 12: Fault Models
Transient Faults
  Single Bit Faults
  Single Byte Faults
  Diagonal faults
Stuck-at Faults
  Bit Faults
  Byte Faults
Instruction Skip Faults

## Slide 13: Fault Injection Techniques
Clock Glitches
Voltage Glitches
Electromagnetic Attacks
Optical attacks
Laser Guns

## Slide 14: Fault Injection Setup : Clock Glitches
Tools Used:
  AES Core Implemented on Xilinx Spartan 3E.
  Tektronix Wave Form (120 MHz) Generator
  Xilinx Chipscope Pro Embedded Logic Analyzer.

## Slide 15: Effect of Clock Glitches on Faults

## Slide 16
When describing a fault attack on any cryptographic primitive, it is important to try and bridge the gap between theoretically and practically achievable fault models

## Slide 17: Fault Attacks on Stream Ciphers
Fault Attacks threaten stream ciphers as well
A number of DFA attacks have been reported on stream ciphers such as Mickey and GRAIN-128
However, not all of these use realistic or practically achievable fault models
The assumption that uniformly random single bit flips can be obtained seems invalid in practical set-ups

## Slide 18: Grain-128 Stream Cipher
eSTREAM hardware port folio finalist
Designed by M. Hell, T. Johansson, A. Maximov and W. Meier

## Slide 19: The XOR Differential Keystream
In order to detect the fault, one needs to identify a pattern in the XOR differential keystream
Prakash Dey, Abhishek Chakraborty, Avishek Adhikari, Debdeep Mukhopadhyay: Improved practical differential fault analysis of grain-128. DATE 2015: 459-464

## Slide 20: Signature of Faults
Key-IV independent Differential Pattern corresponding to a fault

## Slide 21: Signature: A Toy Example

## Slide 22: Generating Polynomial Equations
SAT solver

## Slide 23
SAT Solving Results with timeout of 4 hours

## Slide 24: Fault Injection Technique
Spartan 3A

## Slide 25: What happens in Practice?
All the faults were single bit faults
No multiple bit faults
Single bit faults biased at the 128th NLFSR bit

## Slide 26: Grain-128 : Critical Path

## Slide 27: Practically Achievable Fault Model
Many preceding fault attacks on stream ciphers assume a uniformly random fault distribution
However, fault injections using set-up time violations via clock glitches, for example, would lead to a very biased fault distribution since it is the critical path that would be violated each time
So it would not be practically feasible to obtain the same fault coverage as claimed under the uniform fault assumption

## Slide 28: A More Realistic DFA of Grain-128

## Slide 29: Introducing k- neighborhood faults

## Slide 30: Summary of the Attack
Actual chip results of clock glitch induced faults on a stream cipher (Grain-128) were discussed
Occurrence of biased faults at a single bit
Existing single bit fault based DFA on Grain-128 will not be feasible
Modified fault injection technique: Combining the effect of the clock glitches and also the shift in the registers
Revisiting the DFA algorithm on Grain-128: Relaxed fault model with key recovery possible for k-neighborhood fault

## Slide 31: Conclusions for Part 1
Fault Analysis
Adversary injects faults into cryptosystems and analyzes the faulty output to recover the key
Easy to perform, does not necessarily require high end equipment
Must design efficient countermeasures against fault attacks
Weakens even mathematically robust cryptosystems

## Slide 32: Differential fault ANALYSIS OF BLOCK CIPHERS
PART 2

## Slide 33: AES Algorithm: Our Target Cipher
AddRoundKey
SubBytes
ShiftRows
MixColumns
AddRoundKey
SubBytes
ShiftRows
AddRoundKey
1st Round
Repeat Nr -1 Round
PlainText
CipherText
First 9 Rounds
RoundKey
RoundKey
RoundKey
Last Round

## Slide 34: Effect of Error on AES
Plaintext: 32 43 f6 a8 88 5a 30 8d 31 31 98 a2 e0 37 07 34
128-bit key: 2b 7e 15 16 28 ae d2 a6 ab f7 15 88 09 cf 4f 3c
Ciphertext: 39 25 84 1d 02 dc 09 fb dc 11 85 97 19 6a 0b 32
A single error in the plaintext: 30 43 f6 a8 88 5a 30 8d 31 31 98 a2 e0 37 07 34
Results in the ciphertext: c0 06 27 d1 8b d9 e1 19 d5 17 6d bc ba 73 37 c1
A single error in the key: 2a 7e 15 16 28 ae d2 a6 ab f7 15 88 09 cf 4f 3c
Results in the ciphertext: c4 61 97 9e e4 4d e9 7a ba 52 34 8b 39 9d 7f 84
A single-bit error results in a totally scrambled output
Source : Koren and Krishna, Morgan-Kaufman 2007

## Slide 35: Illustration of a DFA
PLAIN TEXT
ENCRYPTION
ALGORITHM
FAULT FREE
CIPHER TEXT
PLAIN TEXT
ENCRYPTION
ALGORITHM
FAULTY
CIPHER TEXT
ANALYSIS
FAULT INDUCTION

## Slide 36: Types of DFA
Attack Location:
  Targeting the Data Path: Assume that the fault occurs in the AES data path.
  Targeting the AES Key Schedule: Assume that the fault occurs in the AES Key-schedule.
Fault Model:
  Single Byte
  Multiple Byte

## Slide 37: Single Byte Faults in known DFAs
Single Byte Fault
  Attacker induces fault at the input of the 8th round in a single byte
  Fault value should be non-zero but can be arbitrary
Relaxing the requirements make the attack more practical
  No knowledge required of the fault value
  Lesser bytes needed to be faulty
  Lesser faulty cipher texts required

## Slide 38: State of the Art: DFA in DataPath (AES-128)
Piret et. al 2003 (CHES): 2 faults for unique key, Time Complexity: 240
Mukhopadhyay 2009 (Africacrypt): 2 faults for unique key, Time Complexity: 232; showed attack possible with 1 fault.
Tunstall, Mukhopadhyay, Ali 2011 (eprint, WISTP): 1 fault, key space: 28, Time Complexity: 232
Ali, Mukhopadhyay 2011 (eprint):Time Complexity: 230
Subidh Ali, Debdeep Mukhopadhyay, Michael Tunstall: Differential fault analysis of AES: towards reaching its limits. J. Cryptographic Engineering 3(2): 73-97 (2013)

## Slide 39: A Practical Scenario: An Iterated AES Architecture
AES Round
Clk line
PLAINTEXT
STATE REG
STATE REG
An Attacker can time his attack by counting the
number of clock cycles : Control on Fault Timing
CIPHERTEXT

## Slide 40: Principle of the Attack
First, consider a single byte arbitrary fault at the input of the 9th round.
ISB : Inverse Sub Byte
We develop a filter, which takes as input the faulty and fault free ciphertext.

## Slide 41: Propagation of Fault Induced
f
f’
f’
2f’
f’
f’
3f’
F1
F2
F3
F4
F1
F2
F3
F4
9th Round Byte
Sub
9th round
ShiftRow
9th Round
MixColumn
10th Round
ByteSub
10th Round ShiftRow

## Slide 42: The Patterns Gives the Following Equations
ISB(x1+K1)+ISB(x1+F1+K1)=
2[ISB(x2+K2)+ISB(x2+F2+K2)]
ISB(x2+K2)+ISB(x2+F2+K2)=
ISB(x3+K3)+ISB(x3+F3+K3)
ISB(x4+K4)+ISB(x4+F4+K4)=
3[ISB(x2+K2)+ISB(x2+F2+K2)]

## Slide 43: Important Points
No dependency on the fault value.
Finds out the key using two faulty encryptions with a probability of around 0.99
Rest of the cases a third faulty cipher text is needed
Time Complexity is 216.
One byte fault reveals 4 key bytes.
  To obtain the entire key, 4 faulty cipher texts needed.

## Slide 44: When the Fault is Induced in the 8th Round…
Fault is induced at the input of 8th round
A one byte disturbance creates a 4 byte fault at the input of the 9th round
Let us trace the disturbance through the last 3 rounds
Equations of similar nature…

## Slide 45: Propagation of Fault Induced
f
f’
f’
2f’
f’
f’
3f’
F1
F2
F3
F4
F1
F2
F3
F4
8th Round
Byte Sub
8th round
ShiftRow
8th Round
MixColumn
9th Round
ByteSub
9th Round
ShiftRow
2F1
F4
F3
3F2
F1
F4
3F3
2F2
F1
3F4
2F3
F2
3F1
2F4
F3
F2
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A13
A14
A15
A16
A1
A2
A3
A4
A5
A6
A7
A8
A9
A10
A11
A12
A16
A15
A14
A13
9th Round
MixColumn
10th Round
Byte Sub
10th Round
Shift Row

## Slide 46: The Patterns Gives the Following Equations
ISB(x1+K00)+ISB(x1+A1+K00)=
2[ISB(x8+K13) +ISB(x8+F2+K2)]
ISB(x8+K13)+ISB(x8+A5+K00)=
ISB(x11+K22)+ISB(x11+A9+K22)
ISB(x14+K31)+ISB(x14+A13+K31)=
3[ISB(x8+K13)+ISB(x8+A5+K13)]

## Slide 47: For the Other Key Bytes…
  Similar equations are derived for the other key bytes
For all the equations the worst case
complexity is around 28 to 29.
Two faulty cipher text pairs reveal the
exact key with a high probability.

## Slide 48: Can the Attack Work with One Faulty Ciphertext?
With one faulty cipher text:
  Number of possible values per 4 bytes of the key is around 28.
  There are 232 possible candidates for 128 bits of the AES key.
  Brute force key is thus possible!
DebdeepMukhopadhyay, An Improved Fault Based Attack of the Advanced Encryption Standard. AFRICACRYPT 2009: LNCS 5580, pp 421-434

## Slide 49: Why 232?
On an average there is one solution to the equation:
  S-1(x) ^ S-1(x ^ α)=β
Thus for one value of δ1there is 1 value for k1, k8, k11, k14 which satisfies the equations.
Thus for all the 28 values of δ1, there are 28 values for k1, k8, k11, k14.
Thus the total size of AES key is 232

## Slide 50: Comparison of Existing Fault Attacks
Reference | Fault Model | Fault Loc. | #Faulty CT
Blomer | Force 1 bit to 0 | Chosen | 128
Giraud | Switch 1 bit | Any bit of chosen bytes | 50
Giraud | Disturb 1 byte | Anywhere among 4 bytes | 250
Dusart | Disturb 1 byte | Anywhere between last 2 MixColumn | 40
Piret | Disturb 1 byte | Anywhere between 7th& 8th round MixColumn | 2
Mukhopadhyay | Disturb 1 byte | Anywhere between 7th round MixColumn and last round input | 2

## Slide 51: Comparison with Existing Fault Attacks Exploiting Key Scheduling
Reference | No. of fault injection points | No. of faulty encryptions | Brute force search
Takahashi et. al. (NTT Lab) | 1 2 3 | 2 4 7 | 218 216 0
Takahashi et. al. (NTT Lab) | 1 3 | 2 7 | 240 0
Our Attack | 1 1 | 2 1 | 0 232

## Slide 52: Improvement of the Attack
Current research shows that the AES key size can be reduced from 232 to 28 for a single byte fault.
The small complexity of the attack makes it feasible on real life FPGA implementations of AES using less sophisticated techniques, like clock glitching.
Michael Tunstall, Debdeep Mukhopadhyay, S,Ali, Differential Fault Analysis of the Advanced Encryption Standard using a Single Fault, Cryptology ePrint Archive: Report 2009/575, WISTP 2011

## Slide 53: Drawbacks of Existing DFA
Requires 232 brute-force search
Time complexity O(232).

## Slide 54: Improving The DFA
The attack is improved in two ways:
    Reduce the search space of the attack
    Reduce the time complexity of the attack

## Slide 55: Reducing the Search space
Search space reduced in two phases.
First phase:
    Find the 232 candidates of 10th round key.
Second phase
    Deduce four differential equation from differences {2f’,f’,f’,3f’}.
    Reduce the 232 candidates to 28 using the four differential equation.

## Slide 56: Reducing the search space
Differential Equation
Find 232 candidates K10
2128
232

## Slide 57: Reducing the Search space
Differential Equation
Find 232 candidates K10
Find 232 Candidates of K9 using keyschedule
Reduce K9 to 28 candidates
2128
232
keyschedule
Differential Equation
28

## Slide 58: Reducing the Search space
Differential Equation
Find 232 candidate K10
Find 232 Candidates of K9 using keyschedule
Reduce K9 to 28 candidates
Get the master key by 28 brute-force search
2128
232
keyschedule
Differential Equation
28

## Slide 59: Results
Requires 28 brute-force search.
Time complexity 232

## Slide 60: Reducing Time Complexity
Existing DFA required to test 232 candidates of K10 by the 8th round differential equation.
(1)
(2)
(3)
(4)
Equations (2) and (3) does not contain key byte k0 and k1

## Slide 61: Reducing Time Complexity (Cont.)
First and the fourth quartets
Second and third quartets
Test by equation (2) and (3)
Test by equation (1) and (4)

## Slide 62: Results
Time complexity of the attack reduced to 230 from 232
Attack is four times faster.
Ali, Mukhopadhyay 2011 (eprint):Time Complexity: 230

## Slide 63: Effect of clock glitches on Faults: Are these faults practical?
DebdeepMukhopadhyay, "A New Fault Attack on the Advanced Encryption Standard Hardware”, ECCTD 2009, Antalya, Turkey (Invited Paper ).

## Slide 64: Multi-byte Fault Attacks on AES

## Slide 65: AES Algorithm
AddRoundKey
SubBytes
ShiftRows
MixColumns
AddRoundKey
SubBytes
ShiftRows
AddRoundKey
1st Round
Repeat Nr -1 Round
PlainText
CipherText
First 9 Rounds
RoundKey
RoundKey
RoundKey
Last Round

## Slide 66: Fault Model Used
Multi Byte Faults (more practical)
  Attacker induces fault at the input of the 8th round in some bytes
  Fault value should be non-zero but can be arbitrary
Improves the fault coverage.

## Slide 67: Diagonal of AES State Matrix
Diagonal: A diagonal is a set of four bytes of the state matrix,
where diagonal i is defined as follows:
According to the above definition and with reference to the state matrix of AES
(refer figure) we obtain the following four diagonals.

## Slide 68: Fault Models
M0: One Diagonal affected.
M1: Two Diagonals affected.
M2: Three Diagonals affected.
M3: Four Diagonals affected.

## Slide 69: Fault Injection Setup
Tools Used:
  AES Core Implemented on Xilinx Spartan 3E.
  Agilent Wavefrom (80 MHz)Generator
  Xilinx Chipscope Pro Embedded Logic Analyzer.

## Slide 70: Equivalence of Faults according to M0
Faults induced in Diagonal D0 at the input of 8th round AES are all equivalent.

## Slide 71: Inter-relationships depending on the Diagonals affected

## Slide 72: Equations if Diagonal D0 is affected
There are in total 4 such systems of equations for a diagonal D0.
Each system of equation gives 28 keys on an average.
AES key size gets reduced to 232.
If the attacker does not know which diagonal is affected, then key size is
4.232=234.

## Slide 73: Fault Injected across 2 Diagonals (Fault Model M1)

## Slide 74: Equations if Diagonals D0 and D1 are affected
The equation reduces the space of the 4 key bytes of AES to 216
Two faulty ciphertexts reduce it to a unique value on an average (experimental result).

## Slide 75: Fault Injected across 3 Diagonals (Fault Model M2)

## Slide 76: Equations if D0, D1 and D2 are affected
The equation reduces the space of the 4 key bytes of AES to 224
Four faulty ciphertexts reduce it to a unique value on an average (experimental result).

## Slide 77: Experimental Results
ATTACK REGION

## Slide 78: DFA on AES Key-schedule vs DFA on AES datapath
Faults are induced in the Key-schedule.
Attacks on Key-Schedule show that a single byte fault, in the AES-128 keyschedule, reduces the AES key size to 28 values:
  This result is analogous to the single byte fault induction in the AES-128 datapath, where also the remaining key size is 232
  However the time complexity in this present attack is 235, while for the datapath it was 230

## Slide 79: Reduction Proof for Optimality
AdvDFAstate: Adversary against AES performing DFA on state.
AdvColn: Classical Adversary on AES.
Classical adversary searches for plaintexts P and P’ such that after a particular round r a target difference ΔS is created. Probability: Pr(ΔS ).
  KS: Key space of AES wrt. classical cryptanalysis.
  Kl: Key space of AES wrt. DFA
  Kl≥KSPr(ΔS ).
Ali, Mukhopadhyay, Tunstall: Differential Fault Analysis of AES: Towards Reaching its Limits, Cryptology eprint 2012 (JCEN)

## Slide 80: Optimal limit for a byte fault DFA
Assuming, Ks=2128.
ΔS: Single Byte difference at the input to the eighth round.
  Pr(ΔS)=2-120.
  Therefore, Kl=2-1202128=28.
This analysis has been found to work for single byte fault attacks on AES-192, 256 and also for multiple byte faults.
Similar analysis can be also performed for DFA on key-schedules.

## Slide 81: DFA of AES: Summary
Single fault for unique key recovery, Key Space: 28 , Time Complexity: 232
Tunstall, Mukhopadhyay, Ali (WISTP 2011)
2011
2 faults for unique key recovery, Time Complexity: 232
Mukhopadhyay (AfricaCrypt 2009)
2009
2003
Demonstrated attack possibility with a single fault
Ali, Mukhopadhyay (eprint 2011) further reduced the time complexity to 230
Piret et. al. (CHES 2003)
2 faults for unique key recovery, Time Complexity: 240

## Slide 82: DFA Complexities

## Slide 83: Conclusions for Part 2
Faults can be catastrophic for ciphers.
The leakage is so strong that all conventional ciphers are vulnerable against fault attacks.
Important to design suitable countermeasures: of particular interest to smart card industry
This brings a new spectrum to the design philosophy of ciphers to prevent fault analysis.

## Slide 84: Countermeasures versus Biased Faults – Pushing the Limits
PART 3

## Slide 85: Countering Fault Attacks
Whose fault is It?
Is the flaw in the algorithm?
Is the flaw in the implementation?
How can Countermeasures be built?
Does Classical Fault Tolerance work?

## Slide 86: Detection Based Countermeasures
Also known as Concurrent Error Detection (CED) techniques
Use various kinds of redundancy to detect faults
Vulnerable to attacks in the comparison step itself
Vulnerable to biased fault attacks

## Slide 87: The Basic Principle of CEDs

## Slide 88: Examples of CED
Information Redundancy – Robust Codes
Time Redundancy
Hardware Redundancy
Hybrid Redundancy - REPO
Source : Guo et. al. , Security analysis of concurrent error detection against differential fault analysis – Journal of Cryptographic Engineering, 2014

## Slide 89: Error Detecting Codes (EDCs)
First generate check bits
For each operation within encryption predict check bits
Periodically compare predicted check bits to generated ones
Predicting check bits for each operation - most complex step
  Should be compared to duplication
Examples of EDC – parity based and residue checks
Can be applied at different levels – word, byte, nibble
Source : Koren and Krishna, Morgan-Kaufman 2007

## Slide 90: Parity-based Code for AES
Operations operate on bytes so byte-level parity is natural
ShiftRows: Rotating the parity bits
AddRoundKey: Add parity bits of state to those of key
SubBytes: Expand Sbox to 2569 – add output parity bit; to propagate incoming errors (rather than having to check) expand to 5129 – put incorrect parity bit for inputs with incorrect parity
MixColumns: The expressions are:
where is the msb of
the state byte in position i,j
Transformation
Transformation Input (input state matrix)
Transformation Result (output state matrix)
Parity Bit(s)
Parity Prediction
Predicted Parity Bit(s)
Source : Koren and Krishna, Morgan-Kaufman 2007

## Slide 91: Does Detection Always Guarantee Security?

## Slide 92: The Time Redundancy Countermeasure
  S.Patranabis, A.Chakraborty, P.H.Nguyen and D.Mukhopadhyay. A Biased Fault Attack on the Time Redundancy Countermeasure for AES. In Proceedings of Constructive Side Channel Analysis and Secure Design 2015 (COSADE 2015), Berlin, Germany, April 2015

## Slide 93: Against Double Fault Attacks : Detection

## Slide 94: Against Double Fault Attacks: Misses

## Slide 95: Beating The Countermeasure
Improving fault collision probability
  Enhancing the probability of identical faults in original and redundant rounds
Two major aspects
  The size of the fault space
  The probability distribution of faults in the fault space
A smaller fault space enhances the fault collision probability
A non-uniform probability distribution of faults in the fault space also enhances the fault collision probability

## Slide 96: Uniform Fault Model
All faults are equally likely

## Slide 97: Biased Fault Model
A total of n faults possible under a fault model F
Each fault fi has a probability of occurrence Pr[fi]
Let V be the variance of the fault probability distribution
Degree of Bias of a fault model increases with increase in V
Fault Model | Pr[f1] | Pr[f2] | Pr[f3] | Pr[f4] | Pr[f5] | Pr[f6] | Pr[f7] | Pr[f8] | V
1 | 0.125 | 0.125 | 0.125 | 0.125 | 0.125 | 0.125 | 0.125 | 0.125 | 0
2 | 0.225 | 0.200 | 0.175 | 0.125 | 0.100 | 0.075 | 0.050 | 0.050 | 0.004
3 | 0.500 | 0.250 | 0.125 | 0.050 | 0.050 | 0.025 | 0 | 0 | 0.026

## Slide 98: The Fault Collision Probability
With increase in bias, collision probability increases

## Slide 99: The Adversarial Perspective
How can
we exploit
the bias?
But what about practical feasibility?

## Slide 100: Fault Intensity
The impact of fault varies with the tuning of the parameters of the fault inducing process.
More true for low cost equipment.
Insertion of Fault through Clock Glitches:
With increase of clock frequency more bits start getting affected.
We say the fault intensity increases!
Nahid Farhady Ghalaty, Bilgiday Yuce, Mostafa M. I. Taha, Patrick Schaumont: Differential Fault Intensity Analysis. FDTC 2014: 49-58

## Slide 101: Differential Fault Intensity Analysis (DFIA)
Combines fault injection and DPA principles
Induces biased faults by varying the fault intensity
Applies a hypothesis test with biased faults
Uses biased faults as the source of leakage

## Slide 102: Steps of a DFIA
The extraction of the key is like a side channel analysis:
Guessing the key correctly helps in observing the bias in the fault distribution

## Slide 103: Attack on the Time redundancy Countermeasure
All faults are restricted to a single byte
Two kinds of fault models
  Situation-1: Attacker has control over target byte
  Situation-2: Attacker has no control over target byte
Control over target byte makes fault model more precise but is costly to achieve
Suitable

## Slide 104: The Fault Injection Set-Up
Time redundant AES-128 implemented in Spartan 3A FPGA
Fault injection using clock glitches at various frequencies
Xilinx DCM to drive fast clock frequency
Internal state monitoring using ChipScope Pro 12.3

## Slide 105: The Attack Procedure
Fault Distribution
Distinguishers used :
  Hamming Distance (HD)
  Squared Euclidean Imbalance (SEI)
Make a key hypothesis k and evaluate the distinguishers
Correct hypothesis gives minimum
and maximum values respectively

## Slide 106: Simulations-1
Identical faults introduced into both original and redundant rounds
Target byte chosen at random
  Same fault for original and redundant computations
  Each fault injection yields a useful ciphertext
Attacks simulated on rounds 8 and 9
Performed separately for each fault model
Simulation results
Number of ciphertexts required to guess the AES key with 99% accuracy

## Slide 107: Simulations-2
Vary the degree of bias in the fault model
  Control the variance of the fault probability distribution
Observe the number of fault injections to get a faulty ciphertext
Two adversarial models:
  Type 1: Perfect control over target byte
  Type 2: No control over target byte

## Slide 108: Simulations-2 (contd.)

## Slide 109: Experimental Results
Useful ciphertexts
Total Fault Injections

## Slide 110: Comments on Detection Schemes
Bias of a fault model can be quantified in terms of the variance of fault probability distribution
Detection based countermeasures are vulnerable against biased fault attacks that are practically achievable

## Slide 111
Fault Tolerance for DFA needs to be revisited?
Cover all of the essential
or
almost all???

## Slide 112: Countermeasures Must Be Augmented
Detection alone does not guarantee security against fault attacks, especially in the wake of biased fault models
Need to augment the countermeasure scheme to tackle biased fault attacks
Two possible strategies:
  Fault Space Transformation
  Infective Countermeasures

## Slide 113: Fault Space Transformation
Ensure that the adversary cannot exploit the biased nature of the fault model
Fault spaces for the original and redundant computations are different
Adversary cannot ensure the occurrence of equivalent faults in the two different fault spaces at the same time.

## Slide 114: Fault Space Transformation to Counter Biased Fault Attacks
Sikhar Patranabis, Abhishek Chakraborty, Debdeep Mukhopadhyay, P. P. Chakrabarti: Using State Space Encoding To Counter Biased Fault Attacks on AES Countermeasures. IACR Cryptology ePrint Archive 2015: 806 (2015)

## Slide 115: The Impact of Transformation
Transforming the fault space implies that the adversary cannot beat the countermeasure by merely introducing the same fault twice
It is most unlikely that the transformed fault space will have a one-to-one correspondence in terms of bias with the original
Mathematically, the expected fault collision probability over all possible transformations is the same as for uniform fault models

## Slide 116: Results on Hardware
Transformation used is the MixColumn of AES
Single Bit Upset (SBU)
Single Byte Double Bit Upset (SBDBU)
Peaks occur at disjoint frequency regions

## Slide 117: Infective Countermeasures
The main initial idea behind infective countermeasures was to diffuse the impact of the fault such that even if the adversary were to attack the comparison step, the state would still be affected

## Slide 118: The Infection Mechanism
Source : Lomne et. al. , On the Need of Randomness in Fault attack Countermeasures – Application to AES, FDTC 2012

## Slide 119: Infective Countermeasures : State of the Art
Tupsamudre et. al. proposed a randomized infective countermeasure in CHES 2014
Since 2014
Gierlichs et. al. proposed in LatinCrypt 2012 a randomized infective countermeasure that totally does away with explicit consistency checks by clever use of random and dummy rounds
2012-2014
Prior to
2012
Fournier et. al. and Joye et. al. suggested infective countermeasure schemes using deterministic diffusion functions
Proved to be inherently insecure by Lomne et. al. in FDTC 2012
Propagation of faults prevents an attacker from being able to conduct any fault analysis of corrupted ciphertexts
Proved to be insecure against attacks on the last round by Battistello et. al. in FDTC 2013 and Tupsamudre et. al. in CHES 2014
Addresses several pitfalls of the earlier infective countermeasure scheme
Does not provide any formal proofs of security
Does not consider attacks where the execution order of instructions could be changed
Used consistency checks between cipher and redundant computations

## Slide 120: CHES 2014 Infective Countermeasure

## Slide 121: CHES 2014 Countermeasure (Contd.)
Correct Computation
Faulty Computation

## Slide 122: Unexplored Territory-1
Formal Proof of Security
  A frequent criticism of infective countermeasures - no explicit formal proof of security

## Slide 123: Unexplored Territory-||
The countermeasure provides security against fault attacks that target the state registers
What about faults that target the execution order of instructions instead?
For instance instruction skip attacks

## Slide 124: Information Theoretic Proof of Security
Single Fault Injection
Infection upon detection of fault destroys any correlation between output differential ∆ and key K
Hence ∆ and K are independent
Sikhar Patranabis, Abhishek Chakraborty, Debdeep Mukhopadhyay: Fault Tolerant Infective Countermeasure for AES : SPACE 2015

## Slide 125: Security Proofs (contd.)
Multiple Fault Injection
  The adversary must introduce the same fault in a redundant-cipher round pair
  Not easy due to the presence of random intermediate dummy rounds in between
The Attack Probability for 30 Dummy Rounds

## Slide 126: Security Proofs (contd.)
The Evaluation
We focus on the event e’ where an adversary introduces the same fault in a redundant-cipher round pair
Set of faults possible for key

## Slide 127: Conclusions for Part 3
Detection based countermeasures work well against classical uniform fault models
Redundancy alone is not enough to tackle biased fault attacks
Fault Space Transformation tries to make sure the adversary cannot introduce the same fault in the original and redundant rounds
Infective countermeasures attempt use intermediate dummy rounds to confuse the adversary and avoid explicit detection steps

## Slide 128: Fault Tolerance at a Granular Level : Idempotent Instruction Sequences
PART 4

## Slide 129: The Instruction Skip Fault Model
The adversary can skip an instruction
Equivalent to replacing instruction by a NOP
Practically achievable on a variety of architectures
  8-bit AVR microcontrollers
  32-bit ARM9 processor
  32-bit ARM Cortex-M3 processor
Variety of injection techniques possible - Clock glitches, EM Glitches, Voltage glitches and Laser shots

## Slide 130: The Attack Idea
What if the adversary skips this step??

## Slide 131: The Attack Procedure
Skip the increment of the round counter after the final redundant round
The last cipher round is replaced by a spurious redundant round
The adversary obtains the output of the 9th round
Replaced by a Redundant Round

## Slide 132: The Information Leakage
Consider the event e that the attacker successfully performs the instruction skip to recover the key

## Slide 133: The Loop Holes
Fixed ordering of redundant and cipher rounds
Fault in the redundant round is only detected in the next cipher round
No check if a redundant round being executed is valid
Round counter is not validated

## Slide 134: Modified Infective Countermeasure
The relative ordering of cipher and redundant rounds is randomized
The intermediate output after each odd computation round is masked
Penultimate computation could be redundant or cipher
In either scenario, instruction skip gives a masked output that has no correlation with the key

## Slide 135: Instruction Skips on the Modified Countermeasure
Must skip two instructions now – the round counter increment as well as the masking steps in two separate rounds
Practically feasible second order fault attack?

## Slide 136: Some Comparisons

## Slide 137
But what about other Instruction Skip instances ??

## Slide 138: Fault Tolerance at the Instruction Level
Injection of faults in two instructions separated by only a few clock cycles is difficult to achieve in practice
Rewrite compiler generated assembly code by replacing each instruction by a sequence of one or more idempotent instructions
All instructions belong to the x86 instruction set and have uniform size of 32 bits
Provides protection against instruction skip attacks in general

## Slide 139: Sample Instruction Replacement Sequences

## Slide 140: Sample Instruction Replacement Sequences

## Slide 141: Impact on Code Size

## Slide 142: Simulation Studies

## Slide 143: Experimental Set-Up

## Slide 144: Experimental Results

## Slide 145: Conclusions for Part 4
Instruction Skips constitute a strong class of fault attacks that allow the adversary to change the flow sequence of the algorithm
It is difficult to design algorithmic countermeasures that can efficiently counter a large number of instances of instruction skip attacks
Fault tolerance using idempotent instruction sequences seems to be a more effective and generic solution against this class of attacks

## Slide 146: Metrics for Fault Analysis
PART 5

## Slide 147: The Need for Metrics
To measure the vulnerability of systems against fault attacks
To make proper security/cost trade-offs

## Slide 148: Timing Violation Vulnerability Factor (TVVF)
Evaluates the vulnerability of a hardware structure to setup time violation attacks
TVVF is probabilistic metric computed on a circuit’s netlist
Comprises of two parts
  The probability of injecting a specific fault in the hardware structure
  the probability of propagating this fault to the output of the structure
Bilgiday Yuce, Nahid Farhady Ghalaty, Patrick Schaumont: TVVF: Estimating the vulnerability of hardware cryptosystems against timing violation attacks : HOST 2015

## Slide 149: Coverage Provided by TVVF

## Slide 150: The Evaluation Methodology
Scope of Vulnerability
The collection of hardware elements that contribute to an exploitable fault
Scope of Propagation
The part of a netlist that contributes to the propagation of such an exploitable fault

## Slide 151: Example : 2-Bit Ripple Carry Adder

## Slide 152: The Scope of Vulnerability
Analysis is done for faults induced using set-up time violations
Circuit is characterized for timing violations and corresponding paths affected at different clock frequencies
The probability of a bit flip is computed as the fraction of the total number of paths that the adversary can practically violate at a given frequency

## Slide 153: The Scope of Propagation
A probability-based observability analysis method is used to compute the probability of propagating an exploitable fault to the output
Gate-Specific computation rules are used to calculate the propagation probability of faults from the input to the output

## Slide 154: The TVVF Calculation
Inputs : Circuit C, Attack Model A
Compute in three steps
  The probability of injecting a given clock glitch period
  The probability of obtaining a bit-flip in each output of SoV depending on the attack model A
  The probability of observing an exploitable fault in the output of the circuit (SOP)
Combine the values for different clock periods and outputs of SOV to obtain final TVVF value

## Slide 155: Merits and Demerits of TVVF
Merits : TVVVF can be used for
  comparing the vulnerability of two hardware implementations to a given fault attack
  comparing the feasibility of two fault attacks on a specific hardware implementation
Demerits :
  Very specific to fault attacks using clock glitches
  Does not talk about the time complexity for larger circuits

## Slide 156: Conclusions for Part 5
Metrics are essential to compare different implementations of the same algorithm with respect to vulnerability to fault attacks
Current metrics depend heavily on fault models and attack techniques
TVVF is a recently proposed metric that can compare across implementations with respect to security against setup time violation attacks
Need more general metrics that are independent of fault injection techniques

## Slide 157: Cryptographer’s Problem!

## Slide 158: Conference on Hardware Security in India!

## Slide 159: Thank You for your attention!!